# SECTION 08 34 73

# QUAD-LEAF BI-PARTING SOUND CONTROL DOORS

- GENERAL

  - DESCRIPTION OF WORK

- Furnish and install Sound Control Doors specified herein and per the locations and orientations shown on the Contract Documents.  Verify all dimensions and requirements and coordinate with other trades as necessary

- Swing Sound Control Doors, Frame and Seals

- Factory supply and glazing of Sound Control Doors (Where Applicable)

- Factory supply and installation of hardware for Sound Control Doors.

- This quad leaf bi-parting door/frame assembly consists of four (4) equal sized leaves:

- The inactive side shall consist of two leaves leaf, secured in the closed position with a bottom mounted and top mounted slide bolt.

- The active side of the door shall include two leaves. The lead door will be equipped with a mortised lockset.

  - RELATED SECTIONS:

- Specified elsewhere:

1.	Section ______:	Administrative Provisions

2.	Section ______:	Furnishing of Hardware

3.	Section ______:	Finish painting of doors

  - QUALITY ASSURANCE

- Acoustic Performance:

- The manufacturer shall submit certified laboratory test results indicating a Sound Transmission Class (STC) rating of at least 50 when tested in accordance with ASTM E90-02 and E413-87.

- Warranty:

- The door system shall be guaranteed against defective materials and/or workmanship for a period of one (1) year from date of acceptance of the installations.

1.4		SUBMITTALS

- Submit shop drawings, manufacture’s data, and product performance certification in accordance with General Conditions.

- Shop drawings:

- Provide full size details of frames and sound gasket components.

- Provide installation details applicable to the construction in which the Sound Control Doors and frames will be installed.

- Indicate construction, sizes, thicknesses, reinforcing, anchoring, and finishes of all materials.

- Manufacturer’s data:

- Provide illustrations and descriptions of all seals and hardware items which will be exposed on doors and frames for design review by Architect and project Acoustics Consultant.

- Provide complete installation and adjustment information.

- Notification of work completion:

- After installation and prior to acceptance testing, provide a letter to the Architect and the project Acoustics Consultant, co-signed by the General Contractor’s project representative, indicating that all Sound Control Doors assemblies have been installed and gaskets have been adjusted to form an airtight seal around the full perimeter of each door panel.

1.5		SEQUENCING AND DELIVERY

- Upon award of contract and before commencement of building construction, submit to the Architect any special requirements (scheduling, flatness of floor, etc.) which are necessary to assure successful installation.

- Protect door systems during transit, handling and storage to prevent damage, soiling, and deterioration.

- Deliver frames to General Contractor with complete installation drawings and instructions for installation by the General Contractor.

- Deliver doors to project site only after the building has been closed in.  Store doors in the building in a dry location and stack in accordance with manufacture’s instructions.

- Protect door assemblies, especially sound gaskets, from damage before, during and after their installation.

- PRODUCTS

  - APPROVED MANUFACTURER’S:

- The acoustical door shall be minimum 2-½”  thick, “QuietSwing”, Quad Leaf bi-parting STC 50 door assembly as manufactured by NoiseBarriers.

Manufacturer:

Noise Barriers								             Phone:     (847) 843-0500

Fax:  		 (847) 843-0501

www.noisebarriers.com

info@noisebarriers.com

Contact:

John Finnegan

Phone: (315) 682-3821

Fax:	  (315) 682-3868

Email:  j.finnegan@noisebarriers.com

Local Representative:

The Huff Company,

a Ketchum and Walton Company					Phone:   (847) 362-7440

Sherwood Terrace

Lake Bluff, IL

Todd Mitchell				          E-Mail: t.mitchell@soundcontrol.com

  - MATERIALS

- Door leaf shall be fabricated form minimum 14 gauge steel. Door shall be filled with sound-absorbing and dampening elements.

- Frame shall be fabricated from minimum 14 gauge steel. Provide frames with anchors and attachments as necessary to transfer loads to surrounding wall construction.

- Acoustic seals: Side and head of doors and frame shall be provided with two (2) sets of self-aligning magnetic-compression seals to hold door in closed position by the magnetic force of perimeter seals.

- Door Bottom: Bottom of doors shall be provided with a continuous, adjustable, teflon coated, neoprene compression seal mortised into the door bottom and designed to compress against floor as door is closed.

- Vision Lights: Factory installed double-glazed windows in dimensions per the door schedule. All glazing shall be installed by skilled workmen at the manufacturer’s facility.

- Hardware:

- Provide hinges for each door.  Finish of hinges shall be US26D.

- Locks, pull handles, push plates, panic exit devices, door closers and other door hardware as specified in the hardware schedule must be furnished and installed by the sound door supplier. Door leaf and frame for each unit shall be prepared to receive security locks as specified in the hardware schedule.

2.3	FABRICATION

- Assemble doors using all welded construction conforming to pertinent requirements of AWS D1-1.  Assembly and adjustment of door, frame, acoustic seals and hinges shall be performed at the factory.  Each entire unit shall be shipped to the job site ready for installation and subsequent operation.

- Reinforce as required to withstand operating loads.

- Using templates furnished by finish hardware.

- Painting and cleaning:

- On surfaces which are inaccessible after assembly, apply protective coating of the manufacture’s standard rust-inhibitive primer.

- After assembly, and prior to inspection, thoroughly clean all surfaces.

- After inspection, and completion of repairs and revisions required by the inspection, apply a shop coat of rust inhibitive primer to exposed surfaces.

3.0	EXECUTION

3.01		EXAMINATION

Before commencing installation, examine the substrate and surrounding conditions to verify that there is nothing to prevent proper and timely execution of the installation.  Start of work shall indicate acceptance of the substrate and surrounding conditions.

3.02 		INSTALLATION

- Installation of door frames, doors perimeter seals, and final adjustments for door operation and for the design attenuation shall be performed by factory trained personnel under the supervision of the manufacturer.

- Install items plumb (or as indicated on the contract documents), straight, square, level, and in their proper elevation, plane and location.

- Adjust all gaskets to achieve an airtight seal around the entire perimeter of each door panel.

- After installation, adjust doors for smooth and easy operation.

- All work shall be complete in every detail and the finished work shall be clean for Architect prior to final acceptance.

3.03	ADJUST AND CLEAN

- Check and readjust operation finish hardware in work just prior to final inspection.  Leave work in complete and proper operating condition.  Remove and replace defective work.

- Immediately after erection, sand smooth all rusted or damaged areas of prime coat and apply touch-up of compatible air-drying primer.

3.04	ACCEPTANCE TESTING

- Before acceptance of the installed Sound Control Door assemblies, and at any time within the project guaranteed period, the Owner, Architect, or project Acoustics Consultant may request that acoustic performance testing of the installations be performed.  Ideally, this testing shall be performed by an independent acoustics consultant at the expense of the  installing contractor under the supervision of the project Acoustics Consultant, and expenses for the project Acoustics Consultant to supervise the testing shall be paid by the Installing Contractor.  Alternatively, the project Acoustics Consulting may be independently retained by the Installing Contractor to perform this testing.

- The installations shall be deemed acceptable if the Sound Control Door assemblies meet or exceed a Noise Isolation Class (NIC) which is not more than six (6) points below the specified STC rating.

# END OF SECTION